## Slide 1: Project 4B
CS111 Discussion 1D

## Slide 2: Project Statement
Get readings from your temperature sensor using the AIO functions of the MRAA library to samples a temperature sensor at a configurable rate
Convert sensor value into a temperature and creates a report for each sample that includes:
time of the sample (e.g. 17:25:58) in the local timezone
a single blank/space
a decimal temperature in degrees and tenths (e.g. 98.6)
a newline character (\n)
Write that report to the stdout (fd 1) and also appends it to a logfile (which it creates on your embedded system) if logging has been enabled with an optional --log=filename parameter.
Use the GPIO functions of the MRAA library to sample the state of the button (from your Grove sensor kit) and when it is pushed output (and logs) a final sample with the time and the string SHUTDOWN (instead of a temperature), then exit.
Note : Use only MRAA AIO/GPIO functions to access your sensors not Grove library functions

## Slide 3: Project Statement
SCALE=F This command should cause all subsequent reports to be generated in degrees Fahrenheit.
SCALE=C This command should cause all subsequent reports to be generated in degrees Centegrade
PERIOD=seconds This command should change the number of seconds between reporting intervals. It is acceptable if this command does not take effect until after the next report.
STOP This command should cause the program to stop generating reports, but continue processing input commands. If the program is not generating reports, merely log receipt of the command.
START This command should cause the program to, if stopped, resume generating reports. If the program is not stopped, merely log receipt of the command.
LOG line of text This command requires no action beyond logging its receipt (the entire command, including the LOG). In project 4C, the server may send such commands to help you debug problems with your reports.
OFF This command should, like pressing the button, output (and log) a time stamped SHUTDOWN message and exit.
Notes: Extend your program to (in parallel with generating reports) accept the following commands from stdin:

## Slide 4: Interfacing with the grove temperature sensor
The Grove - Temperature Sensor uses a Thermistor to detect the ambient temperature.
Attach your Grove Temperature Sensor to the Analog A0/A1 connector on your Grove cape, where it will be addressed as I/O pin #1.
Attach your Grove Button to the GPIO_50 connector on your Grove cape, where it will be addressed as I/O pin #60.
The detectable range of this sensor is -40 - 125ºC, and the accuracy is ±1.5ºC

## Slide 5: Review : poll(2)
Goal: Wait for some event on a file descriptor (for I/O)
Manual Sections
Maximum time that poll() blocks (ms)
# of items in *fds
Success: # of fd with monitored events // Error: -1
Notes: The field events is an input parameter, a bit mask specifying the events the application is interested in for the file descriptor fd. If this field is specified as zero, then all events are ignored for fd and revents returns zero.
The field revents is an output parameter, filled by the kernel with the events that actually occurred. The bits returned in revents can include any of those specified in events, or one of the values POLLERR, POLLHUP, or POLLNVAL. (These three bits are meaningless in the events field, and will be set in the revents field whenever the corresponding condition is true.)
The caller should specify the number of items in the fds array in nfds.
The field fd contains a file descriptor for an open file. If this field is negative, then the corresponding events field is ignored and the revents field returns zero. (This provides an easy way of ignoring a file descriptor for a single poll() call: simply negate the fd field.)
The bits that may be set/returned in events and revents are defined in <poll.h>:
Specifying a timeout of zero causes poll() to return immediately, even if no file descriptors are ready.
The timeout argument specifies the minimum number of milliseconds that poll() will block.
If none of the events requested (and no error) has occurred for any of the file descriptors, then poll() blocks until one of the events occurs.
WHAT IS INT RETURNED ()
HOW IS ERRNO SET?
WHY NOT USE READ ? ALLOW TIMEOUT

## Slide 6: gettimeofday()
returns the time as the number of seconds since the Epoch, 1970-01-01 00:00:00 +0000 (UTC)
(Obsolete – set this to NULL)

## Slide 7: localtime(3)

## Slide 8: MRAA for I/O
Low Level Skeleton Library for Communication on GNU/Linux platforms
Access the shell on the BeagleBone.
-lmraa flag is required in order to access the functions provided by MRAA.

## Slide 9: MRAA for I/O
mraa_aio_context : Opaque pointer definition to the internal struct _aio. This context refers to one single AIO pin on the board.
mraa_gpio_context : Opaque pointer definition to the internal struct _gpio
mraa_gpio_context mraa_gpio_init ( int pin ) - Initialize gpio_context, based on board number
mraa_aio_context mraa_aio_init ( unsigned int pin ) - Initialize an Analog input device, connected to the specified pin.
mraa_result_t mraa_gpio_dir ( mraa_gpio_context dev, mraa_gpio_dir_t dir )

## Slide 10: Initializing Inputs
Ex:
mraa_aio_context tSens;
tSens = mraa_aio_init(1);
mraa_gpio_context button = mraa_gpio_init(60);
mraa_gpio_dir(button, MRAA_GPIO_IN)

## Slide 11: Reading inputs
int mraa_gpio_read ( mraa_gpio_context dev ) : Read the GPIO value. This can be 0 or 1. A response of -1 means that there was a fatal error.
Read the Gpio value. This can be 0 or 1. A resonse of -1 means that there was a fatal error.
int mraa_aio_read ( mraa_aio_context dev ) - Read the input voltage. By default mraa will shift the raw value up or down to a 10 bit value. Returns -1 on error
Read the Grove temp sensor documentation to see calibration factors and example code to cal the temperature from the reading - http://wiki.seeedstudio.com/Grove-Temperature_Sensor_V1.2/

## Slide 12: Close I/O
mraa_result_t mraa_gpio_close(mraa_gpio_context dev) - Will free up the memory used by context and close related file descriptors
mraa_result_t mraa_aio_close ( mraa_aio_context dev ) - Close the analog input context, this will free the memory for the context